IB ACM
Scalable SA
Sean Hefty
Intel Corporation

---
IBACM Startup
IBACM Startup
Uses random delay on startup
  - Controllable through configuration file
- Issues ServiceRecord like query to locate SSA
  - Response includes path(s) to primary SSA service
  - May or may not use actual ServiceRecord – see following slides
- Connects to SSA service
  - Uses RDMA CM with AF_IB support
  - No requirement for IPoIB
  - Possibly use rsockets with direct data placement extensions

---
IBACM  SSA Communication
IBACM  SSA Communication
Register names and IP addresses
  - Alternatives:
    - Use NodeDescription
    - Publish with “ServiceRecord” query
- Resolve PathRecord(s)
  - Pull model to limit impact on compute nodes
  - Response may be sent as ‘message’ or RDMA write
- Event registration
  - SSA pushes changes to compute nodes to reduce latency reporting events

---
Epoch Number
Epoch Number
64-bit value used to identify if changes to the subnet have occurred
  - 0 indicates all cached data should be invalidated
- SSA uses RDMA write to update epoch value on changes
  - Exposed value is only written by SSA
- ibacm compares public and private epoch values to detect changes
- I.e. SSA notifies ibacm of changes, but ibacm pulls changes when convenient

---
Query Path Record(s)
Query Path Record(s)
- Use MAD structures and definitions
- May want to reduce overhead
  - Eliminate RMPP header
  - Do not require 256 byte sends
- Useful for updating single path records or loading half-world

---
Resolve Path(s)
Resolve Path(s)
- Similar to ACM client messaging interface
- Input: name, IPv4, IPv6, path record (LIDs, GIDs)
  - Wildcard could allow for preloading cache
- Output: name, path data (path records + flags)
- Useful for resolving addresses directly into path records
Requires SSA performs address resolution

---
Resolve Path(s) Details
Resolve Path(s) Details
union ep_info {
uint8_t addr[MAX_ADDRESS];
uint8_t name[MAX_ADDRESS];
struct path_record path;
};
#define EP_FLAG_SOURCE (1<<0)
#define EP_FLAG_DEST (1<<1)
struct ep_addr_data {
uint32_t flags;
uint16_t type;
uint16_t reserved;
union ep_info info;
};
input/output use an array of
<flags, type, address>

---
Resolve Path(s) Examples
Resolve Path(s) Examples
Request
  - SRC, IPv4, 192.168.0.100
  - DST, IPv4, 192.168.0.101
- Response
  - SRC | DST, PATH, <path record>
Request
  - SRC | DST, PATH, <path record with SLID/DLID set>
- Response
  - SRC | DST, PATH, <path record>

---
Query Changes
Query Changes
- Identify which entries in cached data should be invalidated
- Input: start/end epoch numbers
- Output: list of names, IPv4, IPv6, LIDs, GIDs
- If change list cannot be determined, report a failure and ibacm service resets
Requires SSA maintains list of incremental updates

---
Events
Events
Request notification of specific events
  - Need to identify events of interest
- SSA records what events have occurred along with the final data
  - Avoid losing events
- SSA sends notifications to end node
- Is event registration outside scope of ibacm?
  - Registration done from kernel component?