OpenSM Scalable SA Plugin
Hal Rosenstock
18-Sept-2012

---
Agenda
Agenda
- Data Needed for PathRecord Calculation
- Plugin State Machine
- Database
  - Initialization
  - Operations/Commands
  - Sections
    - Topology Related
    - Configuration Related
  - Locking versus Double Buffering

---
Data Needed for “Full” PathRecord Calculation
Data Needed for “Full” PathRecord Calculation
- To respond to PathRecord query in an IBA compliant manner, entire path from end to end needs to be “walked”
- Hence, many OpenSM data structures need replication
  - Nodes, Switches, Ports, partitions, etc.
    - Some configuration files and run time settings too
  - Pointers replaced by indices

---
Data Needed for “Full” PathRecord Calculation
Data Needed for “Full” PathRecord Calculation
Subnet assumptions
  - Use 5:1 ratio of hosts:switches (fits 4 level Fat Tree with CBB=1:1 which would actually be 0.19 sw/host)
  - So fully populated subnet (48K LIDs) is 8K switches and 40K host ports (LMC 0)
  - With 2 port HCAs that's 20K nodes
  - Assume 36 port switches
- Over 384M LFTs (MFTs not calculated) and over 80M of SL2VLMappingTables
  - 8K LFTs @ 48K bytes each = 384M
  - 37*36*8 for each switch = 10K/switch = another 80M

---
Analysis
Analysis
- Calculating N2 PR must be distributed
- To achieve linear time need to distribute the calculation
- Traditionally, PR requires traversal of the entire path
  - For MTU, Rate, SL (verification)
- Providing generic routing data to every SAA does not scale
  - As FDB size is N2 (~370MB for 40K nodes)

---
Analysis
Analysis
Relax the requirements by handling topologies with homogeneous switches
  - Avoids the need to know exact route in the network
  - MTU and Rate detected only on SRC/DST
- Possibility of “invalid” PathRecords returned to ULP/application
  - Bad parameters (SL, rate, MTU)
  - Some routing protocols don’t do complete routing
  - Cause some subsequent failure or error (packet drop)

---
Data Needed for “Full” PathRecord Calculation
Data Needed for “Full” PathRecord Calculation
Is there a way to reduce the amount of data ?
  - Don’t walk full path between source and destination
    - Assume homogeneous switches
      - Use subnet wide max MTU and rate rather than per link
      - Only check this and source and destination ports
    - Ignore LID routing so don’t need to distribute FDBs
      - Eliminates need to distribute 384 MB of LFTs
  - SL2VLMapping table patterns ?
    - 80 MB estimated for this currently
    - Does this need to be addressed in initial phase ?

---
Data Needed for Proposed PathRecord Algorithm
Data Needed for Proposed PathRecord Algorithm
For Switches
  - Common MTU and rate
- For CAs
  - NodeInfo(PG), PortInfo(PG), NodeDesc(PG), P_KeyTbl(PG)
    - PG = PortGuid
- For the Network
  - Routing engine specific
    - torus2qos: torus2qos config file (datelines, seeds, etc.)
    - LASH: SL(SLID, DLID) is O(N**2)
  - QoS policy
    - SL(SRC, DST, QoSLevel, DSCP, ServiceID, … )

---
Data Needed for Proposed PathRecord Calculation
Data Needed for Proposed PathRecord Calculation
For the Network (cont’d)
  - Multicast Groups Data: MCMR (MGID)
    - MCG data is overkill so this is optional
- Same subnet assumptions as before
  - Fully populated subnet (48K LIDs) is 8K switches and 40K host ports (LMC 0)
  - With 2 port HCAs that's 20K nodes
  - Assume 36 port switches
- Attributes Needing Distribution
  - NodeInfo
    - (40K + 8K) * 40 = 48K * 40 = 1.875M
  - NodeDesc
    - 28K * 64 = 1.75M

---
Data Needed for Proposed PathRecord Calculation
Data Needed for Proposed PathRecord Calculation
Attributes Needing Distribution (cont’d)
  - PortInfo
    - All ports
      - 40K + (8K * 37) * 64 = 336K * 64 = 21M
    - HCA ports only
      - 40K * 64 = 2.5M
        - This can be reduced as not full PortInfos required
  - P_KeyTbl
    - Assumptions
      - 128 Pkeys per HCA port
      - 8 Pkeys per switch port 0
      - 32 Pkeys per switch external port
        - Don’t need switch external port pkey tables though

---
Data Needed for Proposed PathRecord Calculation
Data Needed for Proposed PathRecord Calculation
Attributes Needing Distribution (cont’d)
  - P_KeyTbl (cont’d)
    - HCA ports only
      - 40K * 256 = 10240K = 10M
        - Further reduced for actual pkeys in use
          - If assume 4 pkeys in use then this is only 40K * 4 = 160K = 0.156M
  - GUIDInfo
    - Used for virtualization
      - Not needed for HPC

---
Data Needed for Proposed PathRecord Calculation
Data Needed for Proposed PathRecord Calculation
Attributes Needing Distribution (cont’d)
  - MCMemberRecord
    - Assume 1034 MC groups
      - 10 groups have all HCA ports as members
      - Remainder of groups (1024) have 3 ports as members
    - 10 * 40K * 52 + 1024 * 3 * 52 = 20.3125M + 0.1523M = 20.465M
      - Reduced by using minimal MC information per port
        - PortGID, JoinState, ProxyJoin
        - 10 * 52 + 10 * 40K * 16 + 1024 * 52 + 1024 * 3 * 16 = 520 + 6.25M + 52K + 48K = 6.35M
- Total
  - 1.875M + 1.75M + 2.5M + 0.156M + 6.35M (optional) = 12.631M (or 6.281M without optional MCMRs) for “expected” HPC subnet configuration

---
Some Other Data Needed for PR Calculation
Some Other Data Needed for PR Calculation
- Some command line options and configuration files
- C15-0.1.3 requires not responding to any MAD if the SM is not in the active state
  - No response if the sm_state is not MASTER, or if the first_time_master_sweep flag (of the subnet) is TRUE – this flag indicates that the master still didn't finish its first sweep, so the subnet is not up and stable yet

---
Plugin State Machine
Plugin State Machine
Trigger off OpenSM events
  - OSM_EVENT_ID_SUBNET_UP
    - Convert database and in separate thread broadcast to SSAs
      - Take internal OpenSM database and convert to scalable SA database
      - Difference operation between two scalable SA databases
  - OSM_EVENT_ID_STATE_CHANGE
    - Is SM state master ?
  - Use any other events ?
    - OSM_EVENT_ID_TRAP for certain traps might indicate subnet change is about to occur
  - Careful about subnet changing during database push
    - Abort database push but periodically need to make sure database has been pushed

---
Database
Database
Scope
  - Sufficient information so able to respond to SA PathRecord queries locally assuming consistent rate and MTU in subnet core
- Distributed
  - Weak data consistency model
  - Currently, single writer (master SM) and multi reader
    - Will this model change when SA subscriptions are supported in a distributed fashion ?
  - Currently push model with exception of failure recovery
- Made up of various sections
  - Topology related sections
  - Configuration related sections

---
Database
Database
“Generation”
  - For each change set
- Section versioning
  - Newer front end can support older back ends within constraints
    - Requires conversion of sections
    - Not a requirement currently
      - This won’t be done initially

---
Initialization
Initialization
Exchange database information (table of sectionss and versions) between front and back ends
  - Which sections are supported ?
    - Sections may be added, changed, removed over time
  - What versions of each section is supported ?
    - Replicate SMP data as “opaque blob” of 64 bytes ?
      - Handle if/when MADs are extended to 2K ?
- Determine
  - Can section(s) and version(s) be supported ?
  - If so, “translation” rules to be used
    - Translation is performed at back ends
    - Initial implementation will reject mismatched sections/versions

---
Operations/Commands
Operations/Commands
Downstream
  - Start generation (change set)
  - End generation (change set)
    - Abort flag to flush change set
  - Flush entire database
  - Flush section
  - Add row to section
    - Row can wildcard section indices (e.g. port number)
  - Delete row from section
    - Row can wildcard section indices (e.g. port number)
  - Modify (existing) row in section
    - Row can wildcard section indices (e.g. port number)

---
Operations/Commands
Operations/Commands
Upstream (future ?)
  - Request entire database
    - Needed for failure recovery ?
  - Request section ?
  - Request incremental update ?
    - Current database generation
    - Initial implementation may be full update to be replaced by some incremental algorithm (which is TBD)

---
Topology Related Sections
Topology Related Sections
For Switches
  - Common MTU and rate
- For CAs (where PG = PortGUID; note that SA is currently LID rather than GID/GUID based)
  - NodeInfo(PG) and NodeDesc(PG)
    - Combined like SA NodeRecord ?
  - PortInfo(PG, port number)
  - P_KeyTable(PG, port number)

---
Topology Related Sections
Topology Related Sections
SM Related
  - C15-0.1.3 requires not responding to any MAD if the SM is not in the active state
    - No response if the sm_state is not MASTER, or if the first_time_master_sweep flag (of the subnet) is TRUE
      - This flag indicates that the master still didn't finish its first sweep, so the subnet is not up and stable yet
- Future
  - SL2VLMappingTable(PG, input port number, output port number) ?
  - GUIDInfo(Base PG)
    - Alias GUID support for SRIOV
  - MCMemberRecords ?

---
Configuration Related Sections
Configuration Related Sections
Which command line options/config files ?
  - QoS policy
    - SL(SRC, DST, QoSLevel, DSCP, ServiceID, … )
  - Routing engine specific
    - torus2qos: torus2qos config file (datelines, seeds, etc.)
    - Port ordering, port shifting, remote GUID sorting ?

---
Locking versus Double Buffering
Locking versus Double Buffering
Database is currently single writer multiple reader
  - Double buffered at front end
- Could also double buffer at back end
  - Writer updates new database
  - Readers access current database
  - Only lock when update current database
    - When new database is complete
    - Just pointer update

---
Locking versus Double Buffering
Locking versus Double Buffering
Use locking ?
  - Granularity of locking
    - Coarse (single lock)
      - Query responses blocked during database update
        - Unclear amount of time
    - Fine grained (per section)
      - More overhead to take/free locks but more parallelism

---
Lockless ?
Lockless ?
Lockless ?
  - userspace RCU is used heavily in the Linux kernel for quite some time now. Userspace RCU is an active project (unlike some of the lockless libraries like liblfds which was last released 29 Dec 09).
    - http://linuxplumbersconf.org/2011/ocw//system/presentations/729/original/Presentation-lpc2011-desnoyers-urcu.pdf
    - http://lttng.org/urcu
  - Supports the following data structures:
    - Mutex-protected double-linked lists
    - RCU lock-free queue
    - RCU lock-free stack
    - RCU split-ordered lock-free resizable hash table
    - RCU red-black tree

---
Lockless ?
Lockless ?
Couldn’t find lockless data structure support for binary or RB trees which is a requirement for scalable SA. For example, liblfds supports the following data structures:
  - Freelist
  - Queue
  - Ringbuffer
  - Singly linked list (logical delete only)
  - Stack
  - Userspace RCU is under LGPL (2.1+) license
  - API is http://git.lttng.org/?p=userspace-rcu.git;a=blob;f=API.txt;h=72430f7b248565ff2508cac3fde7d03914e50810;hb=8bcbd94a60f624c1faae1481fcb0888aec25b481

---
Lockless ?
Lockless ?
Architectures Supported
  - Currently, x86 (i386, i486, i586, i686), x86 64-bit, PowerPC 32/64, S390, S390x, ARM, Alpha, ia64 and Sparcv9 32/64 are supported. Only tested on Linux so far, but should theoretically work on other operating systems.
- Patents
  - The technique is covered by U.S.software patent 5,442,758, issued August 15, 1995 and assigned to Sequent Computer Systems, as well as by 5,608,893, 5,727,528, 6,219,690, and 6,886,162. The now-expired US Patent 4,809,168 covers a closely related technique. RCU is also the topic of one claim in the SCO v. IBM lawsuit.

---
Thank You